Affected Product: 	 		AO-101

Effective Date: 	 		12/27/2012

Serial Numbers affected:  	All prior to 12/27/2012 (Prefix 								VERALE46 - VERALE50)
						(Serial number VERALE51120106 and above are 						not affected)

Service Issue:			Strain relief wire tie on extruder motor 						may cause excessive stress and failure 						of solid wires.

_______________________________________________________________________

INDICATION:

The motion of the X and Z axis causes flexing of the cables leading to the Extruder Motor and Budaschnozzle. Units have been assembled with a wire tie to reduce the effects of this flexing.

We suspect this wire tie can cause excessive forces to be put on the solid wires leading to the Budaschnozzle. Over time these wires may break and lead to failure.

f

CORRECTIVE ACTION:

Immediately remove the wire tie by cutting through it with a diagonal cutters, xacto knife or equivalent. Be careful not to cut any wires while cutting wire tie.

# Text boxes

Wire tie of concern

CAUTION

Take care to not cut through wires