Calibration Procedure Outline
- Quality Check
  - Y Axis
    - Check screws and zips
    - Check pulley
    - Check belt tension and travel
    - Verify position on frame with fixtures
  - X Axis
    - Check screws and zips
    - Check pulley
    - Check belt tension and travel
    - Check position of smooth rod and double bearing holders
    - Examine print head
  - Z Axis
    - Check screws and zips
    - Examine frame connectors for alignment
    - Inspect Z-limit screw, Z-nut holders and drive rods
  - Electronics
    - Inspect wiring for correct positions
    - Verify no insulation in connectors
    - Check terminal screws for tightness
    - Install fan and test for interference
- Load and Test Firmware
  - Flash Rambo
    - Connect USB to PC
    - Power on printer
    - Open Arduino and load correct sketch
    - Upload sketch to Rambo
  - Test Pronter
    - Open Pronterface and connect to printer
    - Home X and Y axis to verify end stops
    - Carefully home Z axis
  - Rough level bed
    - Position bed corner screws
    - Adjust drive rods
- Calibrate Extruder
  - Test extrusion rate
    - Connect with Pronter
    - Set temps
    - Extrude 100mm @ 70mm/min for .35 nozzle, 100mm @ 90mm/min for .5 nozzle
    - Calculate correction difference 800 / X * 100 = difference
    - Re-flash Rambo with new number
    - Test extrusion again
- Level Bed
  - Print bed calibration file
    - Open Pronter and connect to TAZ
    - Load bed calibration file
    - Set temperatures
    - Inspect print
    - Adjust Z-Limit screw, drive rods and bed corners
- Final Testing
  - Bearing burn-in
    - Move printer to staging area
    - Run burnin.gcode file from SD card
  - Print Octopus
    - Preheat printer for ABS
    - Run octo18-0.9.9.gcode from SD card
    - Inspect octopus for anomalies
  - Position for shipping
    - Cut filament above print head
    - Run z_shipping.gcode from SD card
    - Remove SD card, power printer off and move to packaging area