How to: Gluestick

ABS: With the bed at below 50C apply a thick layer of glue, either to clean glass or on top of a previous layer. Be careful that the glue doesn't build up too much on the bed as this will affect the bottom surface quality, and isn't taken into account for the z-compensation. At the beginning of printing, start the bet temperature heating up to 105C. This will cure the glue and lock the part down before it can warp. The part will be easiest to remove when the bed has cooled to 60C.
Start gcode:
G92 E0
M140 S105 ; get bed heating up
G28; home all
M109 S150 ; set to cleaning temp and wait
G1 E-25 F40 ; suck up XXmm of filament
M109 S170 ; heat up rest of way
G1 X60 Y177 F11520 ; move behind scraper
G1 Z0 ; CRITICAL: set to height of top of scraper
G1 X60 Y178 F4000 ; wiping
G1 X95 Y 176 F4000 ; ""
G1 X100 Y178 F4000 ; ""
G1 X105 Y176 F4000 ; move to center
G1 X60 Y178 F4000 ; long wipe
G1 X105 Y177 F4000 ; back
G1 X60 Y177 F4000 ; forth
G1 X105 Y177 F4000 ; back
G1 X60 Y177 F4000 ; forth
G1 X110 Y177 F4000 ; back
G1 Z10 ; raise z
G28 X0 Y0 ; home x and y
G29 ; Probe
G1 X5 Y15 Z25 ; get out the way
M109 S230 ; set extruder temp and wait
G1 Z0 E0 F1000 ; extrude filament back into nozzle
M140 S105 ; get bed temping up during first layer to cure glue
M206 X0.0 Y0.0 Z0.0 ; offset home position for fine tuning