#define EXTRUDE_MINTEMP 170
		#define EXTRUDE_MAXLENGTH (X_MAX_LENGTH+Y_MAX_LENGTH) //prevent extrusion of very large distances.

		+/*================== Thermal Runaway Protection ==============================
		+This is a feature to protect your printer from burn up in flames if it has
		+a thermistor coming off place (this happened to a friend of mine recently and
		+motivated me writing this feature).
		+
		+The issue: If a thermistor come off, it will read a lower temperature than actual.
		+The system will turn the heater on forever, burning up the filament and anything
		+else around.
		+
		+After the temperature reaches the target for the first time, this feature will
		+start measuring for how long the current temperature stays below the target
		+minus _HYSTERESIS (set_temperature - THERMAL_RUNAWAY_PROTECTION_HYSTERESIS).
		+
		+If it stays longer than _PERIOD, it means the thermistor temperature
		+cannot catch up with the target, so something *may be* wrong. Then, to be on the
		+safe side, the system will he halt.
		+
		+Bear in mind the count down will just start AFTER the first time the
		+thermistor temperature is over the target, so you will have no problem if
		+your extruder heater takes 2 minutes to hit the target on heating.
		+
		+*/
		+// If you want to enable this feature for all your extruder heaters,
		+// uncomment the 2 defines below:
		+
		+// Parameters for all extruder heaters
		+//#define THERMAL_RUNAWAY_PROTECTION_PERIOD 40 //in seconds
		+//#define THERMAL_RUNAWAY_PROTECTION_HYSTERESIS 4 // in degree Celsius
		+
		+// If you want to enable this feature for your bed heater,
		+// uncomment the 2 defines below:
		+
		+// Parameters for the bed heater
		+//#define THERMAL_RUNAWAY_PROTECTION_BED_PERIOD 20 //in seconds
		+//#define THERMAL_RUNAWAY_PROTECTION_BED_HYSTERESIS 2 // in degree Celsius
		+//===========================================================================
		+
		+
		//===========================================================================
		//=============================Mechanical Settings===========================
		//===========================================================================

for(int e = 0; e < EXTRUDERS; e++)
		{

		+ #ifdef THERMAL_RUNAWAY_PROTECTION_PERIOD && THERMAL_RUNAWAY_PROTECTION_PERIOD > 0
		+ thermal_runaway_protection(&thermal_runaway_state_machine[e], &thermal_runaway_timer[e], current_temperature[e], target_temperature[e], e, THERMAL_RUNAWAY_PROTECTION_PERIOD, THERMAL_RUNAWAY_PROTECTION_HYSTERESIS);
		+ #endif
		+
		#ifdef PIDTEMP
		pid_input = current_temperature[e];

		@@ -526,6 +530,10 @@ void manage_heater()

		#if TEMP_SENSOR_BED != 0

		+ #ifdef THERMAL_RUNAWAY_PROTECTION_PERIOD && THERMAL_RUNAWAY_PROTECTION_PERIOD > 0
		+ thermal_runaway_protection(&thermal_runaway_bed_state_machine, &thermal_runaway_bed_timer, current_temperature_bed, target_temperature_bed, 9, THERMAL_RUNAWAY_PROTECTION_BED_PERIOD, THERMAL_RUNAWAY_PROTECTION_BED_HYSTERESIS);
		+ #endif
		+
		#ifdef PIDTEMPBED
		pid_input = current_temperature_bed;

		@@ -896,6 +904,66 @@ void setWatch()
		#endif
		}

		+#ifdef THERMAL_RUNAWAY_PROTECTION_PERIOD && THERMAL_RUNAWAY_PROTECTION_PERIOD > 0
		+void thermal_runaway_protection(int *state, unsigned long *timer, float temperature, float target_temperature, int heater_id, int period_seconds, int hysteresis_degc)
		+{
		+/*
		+ SERIAL_ECHO_START;
		+ SERIAL_ECHO("Thermal Thermal Runaway Running. Heater ID:");
		+ SERIAL_ECHO(heater_id);
		+ SERIAL_ECHO(" ; State:");
		+ SERIAL_ECHO(*state);
		+ SERIAL_ECHO(" ; Timer:");
		+ SERIAL_ECHO(*timer);
		+ SERIAL_ECHO(" ; Temperature:");
		+ SERIAL_ECHO(temperature);
		+ SERIAL_ECHO(" ; Target Temp:");
		+ SERIAL_ECHO(target_temperature);
		+ SERIAL_ECHOLN("");
		+*/
		+ if ((target_temperature == 0) || thermal_runaway)
		+ {
		+ *state = 0;
		+ *timer = 0;
		+ return;
		+ }
		+ switch (*state)
		+ {
		+ case 0: // "Heater Inactive" state
		+ if (target_temperature > 0) *state = 1;
		+ break;
		+ case 1: // "First Heating" state
		+ if (temperature >= target_temperature) *state = 2;
		+ break;
		+ case 2: // "Temperature Stable" state
		+ if (temperature >= (target_temperature - hysteresis_degc))
		+ {
		+ *timer = millis();
		+ }
		+ else if ( (millis() - *timer) > period_seconds*1000)
		+ {
		+ SERIAL_ERROR_START;
		+ SERIAL_ERRORLNPGM("Thermal Runaway, system stopped! Heater_ID: ");
		+ SERIAL_ERRORLN((int)heater_id);
		+ LCD_ALERTMESSAGEPGM("THERMAL RUNAWAY");
		+ thermal_runaway = true;
		+ while(1)
		+ {
		+ disable_heater();
		+ disable_x();
		+ disable_y();
		+ disable_z();
		+ disable_e0();
		+ disable_e1();
		+ disable_e2();
		+ manage_heater();
		+ lcd_update();
		+ }
		+ }
		+ break;
		+ }
		+}
		+#endif

		void disable_heater()
		{

void setWatch();
		void updatePID();

		+#ifdef THERMAL_RUNAWAY_PROTECTION_PERIOD && THERMAL_RUNAWAY_PROTECTION_PERIOD > 0
		+void thermal_runaway_protection(int *state, unsigned long *timer, float temperature, float target_temperature, int heater_id, int period_seconds, int hysteresis_degc);
		+static int thermal_runaway_state_machine[3]; // = {0,0,0};
		+static unsigned long thermal_runaway_timer[3]; // = {0,0,0};
		+static bool thermal_runaway = false;
		+ #if TEMP_SENSOR_BED != 0
		+ static int thermal_runaway_bed_state_machine;
		+ static unsigned long thermal_runaway_bed_timer;
		+ #endif
		+#endif
		+
		FORCE_INLINE void autotempShutdown(){
		#ifdef AUTOTEMP
		if(autotemp_enabled)