What Lulzbot mini needs before release

High Priority : MUST be fixed before we release
- Glue stick bed sticking – need to guarantee that our method works at least as well as PET + lulz
  - Current method – glue applied in a thick layer to bed just before start of print, bed @45C, start print heating to 100C at start of first layer
  - Plan of action:
    - test a part prone to warping (long thick wall) in all of our staple materials, and compare the glue method to a printer set up with PET and lulz-juice – in progress
    - refine the glue application or temperature settings if needed
    - test out hips bed cover printed in cluster – in progress
    - Test other bed cover methods (ultem, etc)
- 2 of 11 begonias have started “skipping”. Not really skipping but essentially the same, moving too far during specific lines of the print, then continuing the print. The printers that are skipping are doing it consistently, the ones not doing it have not shown it once.
  - Have so far ruled out firmware, slic3r version, stepper over heating, pololu over heating, usb cord issues, individual rambo mini's. Sounds like it's a problem with one of the harnesses (noise / bad connection in one of the endstops?)
    - plan of action: replace the mini rambos and see if problem persists (it does). Rewire the machines to rule out harness issue.
- Need a thermal switch to prevent a meltdown / fire situation

Lower Priority:
- PID tuning should be re-performed with the blower heatsink cooler
- add holes for upgradability
- increase temp range and decrease countdown length for M109
- get max endstop values into firmware