FAILURE ANALYSIS REPORT

NAME: Brent MacKenzie	DATE: 2/24/2015
ITEM DESCRIPTION: / Lulzbot Mini 3D Printer	SERIAL NO: / Multiple
FAILURE REPORT DATE: Daffodil batch	ORIGIN: Internal

FAILURE MODE/ DESCRIPTION: / “Squish” generally refers to how much the first layer of the print is pressed into the bed of the printer, and too much or too little can cause issues ranging from print artifacts to complete print failure. An acceptable range was determined by R&D that excluded all printers with squish levels high or low enough to cause noticeable artifacts in the print. As of 2/24/2015, 34 printers have fallen outside of this range and have been studied and reworked by R&D while 96% of the Daffodil machines passed with no rework. 4 of the machines reworked in R&D are still presenting squish issues after several days of attempted fixes.	SYMPTOMS: / Printers with oversquish issues present with a skirt height for less than 0.300mm. Squish of less than 0.300mm will cause excessive rippling in the bottom of the part. / Printers with undersquish have a skirt height of more than 0.450mm. Less squish than this will cause the bottom layer of the part to not fill in fully, and can make parts more prone to lifting off of the bed.

OBSERVATIONS & FINDINGS & PICTURES / Individual printers seem to be very consistent, even when displaying significant squish issues. That is to say, an individual printer can have a squish level anywhere within a range of 0.260mm, but that printer will have the same squish level every print to within 0.025mm. / Many printers showed over squishing on just the left side of the bed. This was tracked down to printed prt interference between the x-end and the print head which caused the print head to tip by a small amount when brought to the x=0 position. / How level the print head was seems to have a significant impact on the accuracy of the auto leveling. There's enough play in the way that the print head screws together to tilt it by several degrees side to side. Resetting the print head in an upright position can change the level of squish by up to ~0.10mm / Resetting the bed in place by loosening all 4 corner discs, twisting the bed back and forth and then tightening incrementally up to 5 in*lb / Some printers were hitting the x-max endstop too soon due to print defects or tilted print head, this threw off the leveling by up to ~0.075mm / Some printers had visibly bent couplers. This was usually the result of misalignment between the stepper shaft and the z-rod, and contributed to under squishing in some cases but not all. / In one case, the bed plate seemed to be propped up by the wiper mount, resetting the mount and bed in blace caused over-squish to decrease by around 0.10mm.

CONCLUSION/ ROOT CAUSE: There is not one root cause for the under/over squishing issues, rather it seems to be around a dozen different factors that can affect where a printer prints verses where it measures the bed to be. / Common Causes of squish issues / Over Squish (21 machines) / Couplers loose / Inconsistent torque on corners (resolved) / Print head contacting x-end / Print head crooked / Plastic blobs stopping print head from reaching x-min/x-max / Bed forcing one of the bed corner spacers, causing it to tilt Under Squish (11 machines) / Misalignment between stepper and z-rod / Loose coupler / Thermistor wires routed around / One of the bed corners stripped / Overly tight y-axis / One of the bed corner spacers overly squished

CORRECTIVE ACTIONS/ FIXES	OWNER	COMPLETION DATE
Implement torque specifications for the bed corners	Brent M	2/15
Have couplers rechecked at the final assembly station	Brent M	2/20
Have final assembly check machines for blobs or interference between print head and the x-ends	Brent M	2/24
Redesign printhead or x-ends to eliminate interference when possible	Seth / Brent M	F-batch Mini's
Change bed thermistor wire routing for euphorbia and adjust z-offset to match	Brent M	Soon

Additional recommendations:

Option 1: Offset in eeprom

We add the z-offset into eeprom so that the squish level can be quickly changed on a machine by machine basis through a g-code command. This would eliminate the need for rework of machines, and would enable us to shrink the acceptable squish range considerably in order to improve print quality. This would also allow us the ability to create a “printer tune-up” ohai kit for customers to quickly restore their machine to factory spec in the event that they change something with a toolhead swap or bed replacement.

This would add an estimated extra 2 minutes per machine to our current production, but would save us from a ~1 hour rework on the 4% of machines that require it.

Time this will add to Euphorbia production: 100 additional hours
Time this will save in Euphorbia production: 122.5 hours saved

Option 2: 1 hour rework and sell off stubborn machines as refurb

We could continue with identical firmware and settings on all machines, and triage the machines that continue to have issues. I estimate that we could pass ¾ of over/under squishing machined with a rework of an hour or less, while we might spend days working on the last ¼ and not be able to solve the issue. The remaining 0.5-1% of machines could be passed off to Jamie Lebon to be flashed with custom firmware and sold as refurbished printers.